## Slide 1: II - ERP Analysis

## Slide 2: What is an ERP?
An Event-Related Potential (ERP) is the brain’s electrical response time-locked to a specfic stimulus or cognitive event. ERPs are characterized by:
Polarity: Negative (N) or Positive (P) voltage deflection
Latency: Time from stimulus onset to the peak of the component in ms.
Amplitude: Voltage difference from baseline to peak.

## Slide 3: The visual oddball task
The Paradigm: Subjects watch a stream of frequent «Standard» stimuli (e.g., 80% blue circles, ignored) and rare «Target» stimuli (e.g., 20% red circles, actively counted).
The Result: Averaging the Target epochs reveals:
  P1 : Occipital positive deflection (~ 100 ms after stimulus onset). Early visual cortex response
  P300: Cemtro-parietal positive deflection (~ 300-550 ms after stimulus onset). Context updating and attentional resource allocation

## Slide 4: Averaging
The Problem: A single epoch contains our signal of interest buried under background neural noise.
The Solution: Averaging all epochs within the same condition allows us to cancel random background noise, while the brain’s consistent, time-locked response emerges.
The Rule of Thumb: To get a reliable ERP, we need:
  at least 30 epochs per condition after rejection (the more the better).
  Use the same number of trials per condition when comparing conditions across subjects to avoid SNR confounds.

## Slide 5: Measuring ERP components
There can be three different approaches
Peak Amplitude and Latency: Find the maximum or minimum value within a predifined time window.
Mean Amplitude: Average the voltage across a time window centered on the component. More stable than peak measures because it is less sensitive to single-point noise.
Area Under the Curve: Capturse total response energy rather than just the peak.

## Slide 6: The latency jitter problem
The Problem: On individual trials, the peak of a component doesn’t always occur at exactly the same latency. Thus, when averaging these misaligned peaks, they don’t add constructively, producing a lower and broader waveform.
The Solutions: Single-trial analysis; peak latency per subject before group averaging; time-frequency decomposition.