## Slide 1: 3 – From Waveforms to oscillations

## Slide 2: Why Frequencies
ERP analysis treats the signal as a series of positive and negative peaks over time. Frequency analysis extracts the rhythmic patterns from the data, and calculates their power change relative to events.
Delta (1 - 4 Hz): Deep sleep, slow cortical potentials
Theta (4 – 8 Hz): Working memory, cognitive effort
Alpha (8 – 13 Hz): Cortical idling
Beta: (13 – 30 Hz): Motor readiness, active cognition
Gamma (30 -80 Hz): Conscious perception

## Slide 3: Fourier Transform
Core Idea: Any signal can be decomposed into a sum of simple sine waves of different frequencies, amplitudes and phases.
  Power Spectrum: Showst the average power at each frequency across the entire recording
  Stationarity Assumption: FFT assumes the signal’s statistical properties do not change over time.
  Spectral leakage: If the analyzed segment does not contain whole cycles of a given frequency, energy leaks into adjacent frequency.

## Slide 4: Time-frequency analysis
Short-Time Fourier Transform: Slide a fix window across the signal and computes FFT in each window. Time and frequency resolution are fixed and depend on the window size (you cannot have both high time and high frequency resolution simultaneously).
Wavelet Convolution (Morlet wavelets): Convolve the signal with wavelets (sine wave tapered by a Gaussian envelope). At high frequencies the wavelets are narrow (good time resolution), while at low frequency they are wide (good temporal resolution)
Hilbert Transform: Instantenous aplitude and phase are extracted after band-pass filtering to a narrow frequency band. Needs careful filter design.

## Slide 5: Event-related spectral Perturbation (ERSP) and Inter-trial coherence (ITC)
ERSP measures how the power at each frequency changes relative to a pre-stimulus baseline following an event. Positive values indicate power increase (synchronization), while negative values indicate power decrease (desynchronization).
ITC measures whether the phase of an oscillation is consistent across trials ast each time-frequency point. It ranges from 0 (random phase) to 1 (perfect phase alignment).

## Slide 6: Baseline normalization in TF analysis
Power at different frequencies has different scales. There are three ways of normalizing:
  dB Normalization: 10 x log10(power / baseline_power). Most common method. It is symmetric, sensitive to the choice of baseline window. Log transform can amplify small baseline fluctuations
  % change: (power – baseline) / baseline * 100. It’s not symmetric. Can inflate high frequency differences.
  Z-score: (power – mean_baseline) / SD_baseline. Accounts for trial-to-trial variability in the baseline, but it assumes normally distributed baseline power (which is not always the case).